## Slide 1
Design and Analysis of a VFFS Auger Filler Machine
From Theoretical Design to Structural Validation
Preper: Hassan Moqbel Morshed
February 2026

## Slide 2
Introduction & Project Overview
Definition
VFFS (Vertical Form Fill Seal) is an automated packaging system used for powders and granules.
Objective
To design a high-precision Auger Filler system specifically for corrosive materials like salt.
Key Features
High dosing accuracy with Servo-driven precision.
Corrosion-resistant materials (AISI 316L/304) for food safety.
Advanced control system using ESP32 with FreeRTOS.
Mass flow optimization for high-density materials (1300 kg/m³).

## Slide 5
Design Methodology
01
Research
Analyzing material properties and market requirements.
02
Modeling
Modeling volumetric flow and torque needs.
03
CAD Design
3D modeling of Auger, Shaft, Hopper in SolidWorks.
04
Analysis
FEA and DEM simulations for validation.
05
Control
Control logic for Servo and Pneumatic integration.

## Slide 6
Mechanical Design: Auger & Shaft
Auger Specifications
Effective Length: 240 mm (Optimized for precision).
Flight Configuration: 4 full flights for consistent dosing.
Material: AISI 316L Stainless Steel (Food Grade).
Surface Finish: Electropolished to prevent material sticking.
Shaft Design
Material: AISI 304/316L for high torsional strength.
Connection: J-slot and Cross-pin for secure torque transfer.
Maintenance: Tool-less disassembly for rapid cleaning.
Alignment: Precision-machined for zero-vibration rotation.
Figure 1: Auger Filler Assembly Diagram
Figure 2: Dosing Screw Detail and Flow Path

## Slide 7
Volumetric & Mass Calculations
Volume per Revolution
Vrev = π/4 (D2 - d2) × P
D
Outer Diameter of Auger
d
Inner (Shaft) Diameter
P
Pitch of the Auger Flight
Determines the theoretical displacement per cycle.
Mass Calculation
Mass = Vrev × ρ × η
ρ
Material Density (1300 kg/m³)
η
Volumetric Efficiency (≈ 0.95)
Adjusted for material behavior and filling efficiency.

## Slide 10
Torque & Power Analysis
Torque Requirements
Calculated Load Torque: ~0.25 N.m (at motor shaft).
Auger Operating Torque: 4.5 N.m (worst-case).
Safety Factor: 2.5x (ensures reliability).
System provides 19.98N.m at the Auger, exceeding requirements.
Motor Selection
Servo Motor: Panasonic MSMF042L1U1.
Rated Torque: 1.27 N.m.
Gearbox Specifications
Type & Ratio: High-Precision Planetary, 1:20

## Slide 16
Structural Analysis: ANSYS Results
Max Von-Mises Stress
136.8 MPa
Significantly below the material yield strength of 206.8 MPa (AISI 304).
Total Deformation
0.095 mm
Minimal deflection ensures precise clearance between auger and tube.
Safety Factor
1.51
Provides a robust margin for operational fatigue and peak loads.
Analysis Type
Static Structural
Simulated under maximum torque and material pressure conditions.
Engineering Conclusion
The FEA results validate that the Auger design is structurally sound. All stresses remain within the elastic region of the material, and deformations are negligible, ensuring long-term reliability and dosing precision in industrial environments.

## Slide 23
Integrated System Analysis: SolidWorks
Assembly Analysis
Verified torque transfer through the J-slot and Cross-pin connection.
Max Assembly Stress: 127.3 MPa (within safe limits).
Max Displacement: 0.0032 mm (ensures high rigidity).
Confirmed no interference between rotating components during operation.
Cross-Validation
Comparative study between ANSYS and SolidWorks Simulation results.
Metric
ANSYS
SolidWorks
Max Stress
136.8 MPa
127.3 MPa
Safety Factor
1.51
1.62
Max Deflection
0.095 mm
0.0032 mm
High correlation between solvers confirms model reliability.

## Slide 24
Operational Simulation & Motion Analysis
Simulation Objectives
Validation of dual-direction rotation (Auger vs. Agitator blades).
Analysis of material flow behavior and volumetric consistency.
Verification of dynamic stability under high-speed operation.
Optimization of dosing cycle timing and material discharge.
Key Findings
Zero interference between rotating components.
Uniform material distribution within the dosing chamber.
[ INSERT MOTION SIMULATION VIDEO HERE ]
Place the video showing the dual-direction rotation here.

## Slide 28
Bill of Materials (BOM) Summary
Category
Component
Specification / Material
Qty
Mechanical Components
Dosing
Auger Screw
AISI 316L Stainless Steel (Food Grade)
1
Structure
Main Shaft
AISI 304/316L - Precision Machined
1
Storage
Hopper Assembly
AISI 316L - 60° Wall Angle
1
Electrical & Control
Actuation
Servo Motor
Panasonic MSMF042L1U1 (400W, 1.27 N.m)
1
Transmission
Planetary Gearbox
Reduction Ratio 1:20 - High Precision
1
Control
Microcontroller
ESP32 DevKit V1 (Dual-Core)
1
Switching
Solid State Relay
SSR-40DA (40A, 3-32VDC Control)
2

## Slide 30
Assess risks and limitations

## Slide 31
Final results

## Slide 32
Conclusion & Future Work
Project Achievements
Comprehensive structural validation using FEA (ANSYS & SolidWorks).
Optimized Auger design for high-density corrosive materials.
Robust control architecture based on ESP32 and FreeRTOS.
Precise torque and volumetric flow mathematical modeling.
Future Roadmap
Physical prototyping and assembly of the VFFS unit.
Real-world material testing for dosing accuracy validation.
Development of a custom HMI for operational control.
Integration of IoT features for remote monitoring.
Thank You for Your Attention